## Slide 1
KWAME NKRUMAH UNIVERSITY OF SCIENCE AND TECHNOLOGY
COLLEGE OF ENGINEERING
DEPARTMENT OF ELECTRICAL/ELECTRONICS ENGINEERING
DESIGN OF A 16 BIT SINGLE CYCLE MIPS MICROPROCESSOR

## Slide 2: INTRODUCTION
Our microprocessor is based on the MIPS architecture. It is a single cycle processor which basically
Fetches
Decode
Execute
Store/Write Back(optional)

## Slide 3: COMPONENTS OF THE PROCESSOR
Registers
Control Unit
Arithmethic Logic Unit(ALU)
Memory(RAM)

## Slide 4: STAGES OF OPERATION
Instruction Fetch stage.
Instruction Decode Stage
Execution Stage
Memory Access Stage
Write Back Stage (Storage)

## Slide 5: REGISTERS
Registers are all 16 bit.

## Slide 6: MIPS ISTRUCRTION TYPES
MIPS is made up of 3 basic instruction Types
R-Type Instruction
I-Type Instruction (Immediate Type)
J-Type Instruction (Jump)

## Slide 7: FORMAT

## Slide 8: OPERATIONS

## Slide 9: MIPS OPERATIONS
add:
It adds the content of the source register 1 to the contents of the source register 2 and saves it in the destination register.
Operation: $s0 = $s0 + $t0
Syntax: add $s0, $s0, $t0
sub:
It subtracts the content of the source register 2 from the contents of the source register 1 and
saves it in the destination register.
Operation: $s0 = $s0 - $t0
Syntax: sub $s0, $s0, $t0

## Slide 10: MIPS OPERATIONS
and:
It does a bit by bit logical and operation between two source registers contents.
Operation: $s0 = $s0 & $t0
Syntax: and $s0, $s0, $t0
or:
It does a bit by bit logical or operation between two source registers contents.
Operation: $s0 = $s0 || $t0
Syntax: or $s0, $s0, $t0

## Slide 11: MIPS OPERATIONS
slt:
It compares the contents of two source registers. If the content of 1st source register is less than
the second source register, then it sets the value of destination register to 1, otherwise 0
Operation: if ($s0 < $t0)
$s0 = 1
Else $s0 = 0
Syntax: slt $s0, $s0, $t0
lw:
It loads the contents of the memory specified by the offset and saves it into a destination register.
Operation: $s0 = Memory [$s1 + offset]
Syntax: lw $s0, 2($s1)
sw:
It stores the contents of a source register to the memory address specified by the offset
Operation: Memory [$s1 + offset] = $s0
Syntax: sw $s0, 2($s1)

## Slide 12: MIPS OPERATIONS
beq:
It checks if the content of the provided register is equal to the contents of another register or not.
If equal jumps a relative number of instructions else continue.
Operation: if ($s0==$t0) jump to L (Label)
Else go to next line
Syntax: beq $s0, $t0, L
bne:
It checks if the content of the provided register is not equal to the contents of another register or
not. If not equal, jumps a relative number of instructions else continue.
Operation: if ($s0 != $t0) jump to L (Label)
Else go to next line
Syntax: bne $s0, $t0, L
addi:
It can add direct value (constant) with a content of a source register.
Operation: $s0 = $t0 + immediate value
Syntax: addi $s0, $t0, 4

## Slide 13: MIPS OPERATIONS
andi:
It does logical bit by bit and operation with a constant value and a content of a source register.
Operation: $s0 = $t0 & immediate value
Syntax: andi $s0, $t0, 4
ori:
It does logical bit by bit or operation with a constant value and content of a source register.
Operation: $s0 = $t0 || immediate value
Syntax: ori $s0, $t0,
srl:
This operation shifts the content of a register to right by a constant and stores shifted
value todestination register.
Operation: $s0 = $t0 >> 4
Syntax: srl $s0, $t0, 4

## Slide 14: MIPS OPERATIONS
sll:
This operation shifts the content of a register to left by a constant and stores shifted value todestination register.
Operation: $s0 = $t0 << 4
Syntax: sll $s0, $t0, 4
J:
It jumps a relative number of instruction/s specified by given label
Number.
Operation: jump to Label
Syntax: J, L

## Slide 15: THE BUILT PROCESSOR

## Slide 16: CONTROL UNIT

## Slide 17: 1 BIT ALU

## Slide 18: 16 BIT ALU

## Slide 19: ALU CONTROL

## Slide 20: Operation of our ALU
The operation of the ALU is relatively simple and straight forward. Two inputs A and B are connected to the abstracted operation logic circuits. Once there is an input, the ALU executes that particular instruction and return a desired output in 16-bit. The result of the operation is sent into the multiplexer connected to our 16-bit register where it is written to.